## Slide 1: SoC Testing: DFT for Test Optimizations in a Complex Mixed-Signal SoC – Case Study on TI’s TNETD7300 ADSL Modem Device
ECE 7502 Class Discussion
Farah B. Yahya
02/05/2015

## Slide 2: What I was looking for:
How can we improve and speed up the testing of mixed signal SoC?
Source: UVA Center for wireless health
[6] Y. Zhang , JSSC 2013

## Slide 3: Paper Map
[1] Nikila, K.; Parekhji, R.A., "DFT for test optimisations in a complex mixed-signal SOC - case study on TI's TNETD7300 ADSL modem device,“ ITC 2004.
[2] Marinissen, E.J.; …"Towards a standard for embedded core test: an example.” ITC 1999
[3] McLaurin, T.L.; …"The testability features of the ARM1026EJ microprocessor core," ITC 2003.
[4] van Rootselaar, G.J.; Vermeulen, B., "Silicon debug: scan chains alone are not enough," ITC 1999.
[5] Gallagher, P.; …"A building block BIST methodology for SOC designs: a case study," ITC 2001.
[1] and [3] are testability features on specific SoCs
[5] gives a BIST Methodology for SoC design
[2] is a description of a test standard for embedded cores.
[4] focuses more on debugging errors than manufacturing tests.
One step up is a methodology.
Alternative approach: debug structures.
A standard for SoC testing
Notes: [5] Transforms all registers in the design to LSSD (level sensitive scan design) then uses then as shift register latches (SRL)and inserts PRPG (psuedo-random pattern generators) and MISR (multiple input signature response) analyzer and memory BIST for large memories
[2] presents an overview of the embedded core extension to JTAG.
[4] talks mostly about silicon debug and that scan chains are not enough to help debug, structures that detect events within the SoC and pause the SoC

## Slide 4: Briefly Papers
[2] described the P1500 standard for embedded core testing – Mainly defines wrappers around the core and a test language.
[3] described the testing of an ARM chip (only has PLL as analog block)
[4] described the need for additional structures (other than scan) to enable debug

## Slide 5: BIST Methodology [5]
[5] P. Gallagher, ITC 2001

## Slide 6: Chosen Paper
Analog Subsystem
DSL subsystem
DSP subsystem
Networking subsystem
[1] Nikila K., ITC 2003

## Slide 7
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 8: Main Goals
Meet test quality:
  Stuck-at coverage of 95%
  Iddq coverage of 80%
  Transition fault coverage of 85%
  High coverage of all stress tests
  At-speed testing of all memories
  Design for debug
Reduce test cost:
  Simultaneously test all IP blocks
  Simultaneously test analog and digital modules
  Use high-end and low-end testers

## Slide 9: DFT requirements/technique (1)
Test Modes
  Need to cover all the target faults (stuck-at, iddq, transition and burn in).
  Need to run tests in parallel or serially for debug.
Technique:
  Generated test patters for the different target tests.
  Implemented test parallelism
  Defined test interface pins that could be muxed
  Implemented JTAG TAP interface
  Implemented diagnosis and debug mode
[1] Nikila K., ITC 2003

## Slide 10: DFT requirements/technique (2)
Scan Architecture and Design Partitioning
  Need to interface with multiple testers – Number of scan chains that run in parallel is limited by the tester capability.
  Need to have enough control for at-speed testing.
Technique:
  Group scan chains into 4 groups.
  Group scan chains in the same clock domain together.
  Group IP core scan chains together
[1] Nikila K., ITC 2003

## Slide 11: DFT requirements/technique (3)
Common interface for different IP blocks
  Need to run tests in parallel to test manufacturing faults mainly.
Technique:
  Scan chain grouping
  Circuits to generate scan & control signals
  Configuration registers
  Interface to peripheral must be tested
[1] Nikila K., ITC 2003

## Slide 12: DFT requirements/technique (4)
Memory BIST
  Need to run tests in parallel & serially to allow debug
  Need to report status signals.
Technique:
  Enable/Status/Data logging signals for each BIST controller
  Different operating modes to support the different tests

## Slide 13: DFT requirements/technique (4)
[1] Nikila K., ITC 2003

## Slide 14: DFT requirements/technique (5)
At-speed ATPG
  Need to run different scan chains at different frequencies.
  Need to detect delay and transition faults
Technique:
  Group scan chains according to their clock domains.
  Reduce pattern sets by pairing scan groups together
  Conditional scan shift and captures (scan groups can be tested separately)
  Support for scan and functional justified delay testing.
  All multi-cycle and false paths are re-synthesized

## Slide 15: DFT requirements/technique (6)
Analog/Digital partitioning
  Need to run different them concurrently
Technique:
  Four mixed signal tests were defined (Gain error, missing tone performance, corner freq. & prog. gain amp test)
  Divide the digital part of the analog and combine its test with the digital part.
  Isolate the interfaces and control
  Coupling between digital and analog need to be checked

## Slide 16: DFT requirements/technique (7)
Burn in tests
  Need to run for analog and digital in parallel or serially
  Need to report and debug faults.
Technique:
  High level of activity required – need scan patterns,
  Concurrent testing of analog an digital
  Monitor output pin to identify failing chips
  Scan chain can be monitored for debug purposes.

## Slide 17: Results
Scan configuration allowed up to 40% reduction in test patterns required.
53% reduction in test times (excluding burn-in)
[1] Nikila K., ITC 2003

## Slide 18: Discussion questions
On page 775, the authors claim that scan chain balancing improves the test pattern efficiency - why?
Does the data in table 1 match the explanations in the text?
How are the mixed signal tests applied? and checked?
How do they measure the fault coverage in their tests?
What are the novel ideas presented in this paper?
What type of tests can we adopt from this paper to apply to the SoCs we build?

## Slide 19: Papers
[1] Nikila, K.; Parekhji, R.A., "DFT for test optimisations in a complex mixed-signal SOC - case study on TI's TNETD7300 ADSL modem device," Test Conference, 2004. Proceedings. ITC 2004. International , vol., no., pp.773,782, 26-28 Oct. 2004
[2] Marinissen, E.J.; Zorian, Y.; Kapur, R.; Taylor, T.; Whetsel, L., "Towards a standard for embedded core test: an example," Test Conference, 1999. Proceedings. International , vol., no., pp.616,627, 1999
[3] McLaurin, T.L.; Frederick, F.; Slobodnik, R., "The testability features of the ARM1026EJ microprocessor core," Test Conference, 2003. Proceedings. ITC 2003. International , vol.1, no., pp.773,782, Sept. 30-Oct. 2, 2003
[4] van Rootselaar, G.J.; Vermeulen, B., "Silicon debug: scan chains alone are not enough," Test Conference, 1999. Proceedings. International , vol., no., pp.892,902, 1999
[5] Gallagher, P.; Chickermane, V.; Gregor, S.; Pierre, T.S., "A building block BIST methodology for SOC designs: a case study," Test Conference, 2001. Proceedings. International , vol., no., pp.111,120, 2001
[6] Yanqing Zhang; Fan Zhang; Shakhsheer, Y.; Silver, J.D.; Klinefelter, A.; Nagaraju, M.; Boley, J.; Pandey, J.; Shrivastava, A.; Carlson, E.J.; Wood, A.; Calhoun, B.H.; Otis, B.P., "A Batteryless 19 W MICS/ISM-Band Energy Harvesting Body Sensor Node SoC for ExG Applications," Solid-State Circuits, IEEE Journal of , vol.48, no.1, pp.199,213, Jan. 2013

## Slide 20: Glossary
SOC: System on Chip
DFT: Design for test
BIST: Built in self test
VLCT: Very Low Cost Tester